## Slide 1: Performance test and VNAPT

## Slide 2
Purpose of Performance test
Performance test will check the VNA’s performance to make sure it’s all within the specifications, such as output power, CW frequency, harmonic distortion, etc.
The Analyzer’s recommended performance test interval is once each year.
Purpose of VNAPT
VNAPT is designed to automating VNA performance testing in order to ease the process and generate the report automatically.
You can download the VNAPT software for Copper Mountain Technologies website.

## Slide 3
The following example procedure is based on Planar 804/1. Other models will be following a similar procedure with small differences, such as number of ports, frequency range, etc. For details, please refer to Performance Test Manual.
Procedure
Connect VNA to the computer
Start VNA program, wait until the lower right corner shows ‘Ready’
Start VNAPT program
Choose the device and click the blue start button to start

## Slide 4
Required equipment
Equipment similar to the listed can be used provided it satisfies the specifications shown in the table.
NPR-Z51 Thermal Power Sensor is required if automation of output power test is desired.

## Slide 5
Test content
Test procedure can also be found in the Performance Test document, which can be downloaded from Copper Mountain Technologies website.

## Slide 6
Software Interface

## Slide 7
Software Interface

## Slide 8
Software Interface

## Slide 9
Note
Version 1.4.9.22 of VNAPT support Planar 804/1, Planar 808/1, S5048, Planar R54, and Planar R140.
For VNAPT to work properly, COM server need to be registered correctly near the end of VNA software
  Take care during the VNA software installation to register the COM server, which is the last step of the installer. At the prompt “Register COM Automation Server of the application” the box must be checked. A dialogue box indicating successful COM server registration will be displayed.

## Slide 10
Test procedure can also be found in the Performance Test document, which can be downloaded from Copper Mountain Technologies website.
Copper Mountain Technologies partners with several accredited service, repair, and calibration labs across the United States and internationally. Any certified lab can perform the maintenance needed for annual verification and calibration. Please contact us for details on these procedures.
If you have any questions, please e-mail us at support@coppermountaintech.com